## Slide 1: 3D-Printing For Beginners

## Slide 2: Workshop overview
Introduction and Expectations
Goal of the Workshops
Basics of 3D Printing
Introduction to Tinkercad
3D Modeling
Introduction to Ultimaker Cura
Print Preparations
Results and Feedback

## Slide 3: Goals of the workshop
Understanding of the process of 3D printing
Understanding of opportunities and limitations
Basic 3D modeling using „Tinkercad“
Slicing and refining using „Cura“
Printing using Ultimaker S5

## Slide 4: What is 3D printing?
3D printing, also known as additive manufacturing, is a process of creating physical objects from a digital 3D model.
It involves building up layers of material, such as plastic, metal, or resin, until the desired shape or structure is formed.
3D printing can be used in a variety of industries, from product design and prototyping to aerospace and healthcare, and has the potential to revolutionize the way we manufacture and produce goods.

## Slide 5: Possible materials for 3D printing
Plastic
  PLA(Polylactic acid)
  ABS(Acrylonitrile butadiene styrene)
  PETG(Polyethylene terephthalate)
Resin
Ceramic
Metal
Edibles(chocolate etc.)

## Slide 6: Use cases of 3D printing
Rapid prototyping
Automotive industry
Aerospace industry
Medicine & Healthcare
Rehabilitation & Accessibility
3dnatives.com, 25.01.2023
chemanager-online.com, 25.01.2023
wa.de, 25.01.2023
www.trumpf.com, 25.01.2023

## Slide 7: 3D printers in Hylec
Ultimaker S5
Ultimaker 2+ connect

## Slide 8: Different 3D printing processes
FDM (Fused deposition modelling)
DED (Directed energy deposition)
SLS (Selective laser sintering)
SLA (Stereolithography)

## Slide 9: FDM 3D Printing Animation
https://www.youtube.com/watch?v=TZmYTfPfhNE

## Slide 10: Video Demo FDM-Printer

## Slide 11: 3D printing process
Model
Finding a Model that is „Printable“
Editing or Modelling a printable Model(Tinkercad)
Exporting as Mesh
Slice
Slicing and tweaking using a slicer(Ultimaker Cura)
Print
Sending G-code to the printer and printing

## Slide 12: Introduction to Tinkercad
Free CAD-software (computer-aided design)
Beginner friendly
Based on primitive shapes

## Slide 13: Tinkercad Demo
Join the course via following link:
https://www.tinkercad.com/joinclass/PYLJP2DHX
Or using following code:
PYLJP2DHX

## Slide 14: Modelling a keychain
Notes: What is the functional requirements?
What is the structural requirements?
How should the dimentions be defined?

## Slide 15: Reviewing the models
Notes: Is it printable?
Does it need supports?
Does it need refinement/rework after the printing?
How is the structural integrity?

## Slide 16: Introduction to Ultimaker Cura
Free open source slicer-software
Slices the model into different layers
Generates infill and support structure
Generates G-code for printer

## Slide 17: Example Model – Cuddling Owls
Draft 0.3mm 10% Infill ~4 Hrs.
Engineering 0.15mm 10% Infill ~13 Hrs.
Visual 0.1mm 10% Infill ~16 Hrs.
Default 0.06mm 10% Infill ~23,5 Hrs.

## Slide 18: Example Model – Cuddling Owls

## Slide 19: Draft 0.3mm | 10% infill | Adhesion | ~ 4 Hrs

## Slide 20: Engineering 0.15mm | 10% infill | Adhesion ~ 13 Hrs

## Slide 21: Visual 0.1mm | 10% infill| Adhesion ~ 16 Hrs

## Slide 22: Default 0.06 | 10% infill | Adhesion ~ 23,5 Hrs

## Slide 25: Infill Grid

## Slide 26: Infill Grid

## Slide 27: Infill Cubic

## Slide 28: Infill Cubic

## Slide 29: Print preparations in Cura
Lets slice and print!

## Slide 30: Recommendations
Printables.com
Thingiverse.com
Autodesk Fusion 360

## Slide 31: Conclusion and Feedback